## Slide 2
Introduction to Smart Pendant
Sayre Jeannet

## Slide 3
Overview
Why have a Smart Pendant?
Smart Pendant vs Traditional
Features
Hardware
Pendant Options
Software
Hands On
Restrictions
Functions
  Jogging
  Smart Frame
  Easy INFORM
  Visual Limits
  Teaching Points
  Job Editing
  Command Builder
  Playback
  Variables
  IO
Introduction to Smart Pendant

## Slide 4
Introduction to Smart Pendant
Why have a Smart Pendant?
EASE OF USE
To offer a pendant to new customers that is both easy to use and encourages customer participation
Simplified “HMI” interface to allow line operators to easily reset and restart the robots
Responsive touch screen interface allows for greater flexibility and comfort for today’s smart phone users

## Slide 5
Introduction to Smart Pendant
Smart Pendant vs Traditional
Utilizing the latest in modern User Interface design techniques to give users better performance, reduced errors, coherence in information display, action feedback, and assistance with error recovery.
Offers expert functionality that is market leading

## Slide 6
Introduction to Smart Pendant
Smart Pendant vs Traditional
 | YRC Pendant | Smart Pendant
Applications | All | Material Handling, Machine Tending, Injection Molding, Inspection, Assembly
Sale Price | Included with Controller | Same
Platform | Resistive touch screen with many membrane keys | Tablet with Projective Capacitive Touch (PCT) screen that is designed to be hardware independent
Ergonomics | Designed for extended use by a left/right handed person | Designed for shorter duration use by right handed person
Feature Set | All | Limited to meet 80% of handling applications
Customer | Trained robot programmers | Plant engineers and end user operators with limited robotics experience.
Ease of Use | Designed for efficient use by trained programmers | Designed for easy use by novice programmers with little to no training

## Slide 7
Introduction to Smart Pendant
Features: Hardware
• 10.1” WXGA TFT Display
• 1280 x 800 pixels
• LED back light touch panel
• Capacitive Touchscreen
• 215W x 283.5H x 68.5D mm
• Weight 1.12kg
• Drop Tested: 1m
• External Storage: USB memory

## Slide 8
Introduction to Smart Pendant
Pendant Options
YRC Controller + YRC Pendant
Full functionality on Pendant
Full configurability of Controller
Targeting existing customers who know Yaskawa products
OPTION 1
OPTION 2
YRC Controller + Smart Pendant
Subset of functionality on Pendant
Fixed configuration of Controller (with some subset of options)
Targeting new customers with reduced customization needs

## Slide 9
Introduction to Smart Pendant
Smart Pendant Software
The included Software Pendant will be required for Maintenance mode, FSU Settings, and Safety Logic functions

## Slide 10
Introduction to Smart Pendant
Smart Pendant Benefits
Smart Pendant reduces the memorization by guiding a user to enter the relevant instructions, values, and/or procedures
The main menu makes switching among screens a comfortable experience .
Main menu provides easy access to all functionality.

## Slide 11
Introduction to Smart Pendant
Robot Jogging
Robot jogging supported from either touchscreen buttons or membrane keys interchangeably
Membrane Keys on the right are dynamically labeled with a black slide out bar

## Slide 12
Introduction to Smart Pendant
Supported Jogging Modes
HC10 Exclusive
Smart Pendant Exclusive

## Slide 13
Introduction to Smart Pendant
Smart Frame
PATENTED
Uses the internal Inertial Measurement Unit (IMU) and compass inside the pendant to determine the user’s position relative to the robot.
The system requires initial calibration by standing directly in front of the robot and facing the robot.
Uses intuitive directional buttons to move relative to the operator
Motion is relative to the user
Away
Right
In each of these four examples, the robot will move the same direction
Towards
Left

## Slide 14
Introduction to Smart Pendant
Easy INFORM
Descriptive commands no longer require users to memorize abbreviations
A favorites bar allows for easy access to the most commonly used commands
Classic View
Smart Pendant View

## Slide 15
Introduction to Smart Pendant
Visual Limits
Joint Jogging mode
  Touch screen jogging buttons show current joint position relative to maximum range below each button.
  Yellow – Jogging buttons turn yellow when the joint is close to the maximum limit
  Red – Jogging buttons turn red when the axis limit has been reached.
  Indicator in the top right corner of the jogging screen shows limits for all axis, regardless of jogging type selected
Axis limits shown via color
Axis Range Indication

## Slide 16
Introduction to Smart Pendant
Teaching Points
Teach button located above jogging keys
The right half of the teach button indicates the taught motion type
Motion type can be cycled through by touching the selected motion type
No longer required to press INSERT
Will insert motion above “End Job” and not produce error if user tries teach a point while “End Job” is selected

## Slide 17
Introduction to Smart Pendant
Job Editing
Easier than ever with touch to edit functionality
Modern gear symbol allows users to “detail edit” any line of code
Darker Highlighting Indicates Editable Field
Copy, Cut, Paste, Undo, and Redo functionality easily accessible in the top right corner of the job edit window

## Slide 18
Introduction to Smart Pendant
Command Builder
Guides a user to inserting basic commands
  Set a Value
  Read a Value
  Wait for a Value
Designed for first time users yet to learn command names

## Slide 19
Introduction to Smart Pendant
Playback
Interface designed to give relevant information during playback:
Allow users to easily monitor variables, positions, and IO during runtime with Watch Windows
Code as it’s run
Robot’s virtual position along the path
Moving, Power On, Playback, and Servo On time information

## Slide 20
Introduction to Smart Pendant
Variables & IO
Allow easy viewing of multiple fields, naming relevant signals or variables, and easy modification via touch screen interface

## Slide 21
Introduction to Smart Pendant
Multi-Lingual Support
Supports Multiple Languages with more to come

## Slide 22
Introduction to Smart Pendant
Conflicts and Restrictions
Smart Pendant is quickly adding functionality but does not yet support all the same features as the standard YRC1000 pendant
MotoSight 2D and other Macro enabled products are not yet supported
Pendant applications are not backwards compatible with older pendants
The software pendant (included at no extra cost) can be run via an ethernet connected laptop.
More Features Coming Soon!
Functionality | Smart Pendant | Software Pendant
Jogging | X | 
Conveyor Tracking |  | X
IO & Error Handling | X | 
User Frames / Interference Zones | X | 
Setting of ABSO Data |  | X
PFL/Tool Setup | X | 
Functional Safety / Safety Logic Settings |  | X