## Slide 2
YRC1000 Review
Sayre Jeannet

## Slide 3
New Features and Functionality
VMAX function
3D graphical window
Programming Pendant Interface Improvements
Simplification of multiple condition programming
Robot operating state monitoring
Job monitoring function
Robot monitoring
Pendant oscilloscope improvements
YRC1000 Review

## Slide 4
VMAX Tag
Designed to allow a programmer to move in a linear motion at maximum speed.
Speed is not constant but optimized for the robot’s current posture.
What’s the difference between MOVL & MOVL VMAX?
MOVL & MOVL VMAX both travel along a linear path.
MOVL speed is specified in mm/sec while MOVL VMAX speed is specified in % of maximum speed.
How do I access the VMAX tag?
Detail edit screen
YRC1000 Review
VMAX is based on %

## Slide 5
3D Graphics Window
View the robot’s programmed path in a job
3D viewing of Safety Range Limits (Cuboid/Planar/Prism)
Viewing of Tool Interference Zone
3D View Setup
Safety Function > Robot Range Display
3D View Access
Robot > 3D Graphics
YRC1000 Review

## Slide 6
Programming Pendant Interface Improvements
Text Copy & Paste now available
Long press the screen to allow easy access to zooming functionality
Numeric touch screen keypad available
YRC1000 Review

## Slide 7
Simplification of Multiple Condition Programming
Multiple AND/OR conditions can be applied to a single logical instruction
Conditional expressions allow up to 15 different conditions based on AND/OR operators
YRC1000 Review
DX200 | YRC1000

## Slide 8
Robot operating state monitoring
Allows for monitoring of:
  Operation time
  IO waiting time
  Energy saving time
  Alarm related stop time
Multiple Time Intervals Available
  Hourly (max 5 days)
  Daily (max 100 days)
  Monthly (max 60 months)
YRC1000 Review

## Slide 9
Job Monitoring / Diagnosis
Job Monitoring allows for monitoring of:
  Number of times that job has been executed
  The moving/playback time per job
  Stopping time related to IO
  Time spent in energy saving mode
Job Diagnosis / Analysis
  Duty cycle
  Max speed & torque
  Average speed & torque
YRC1000 Review

## Slide 10
Robot Monitoring
Robot Monitoring allows for threshold monitoring of:
  Torque
  External Force
  Axis Speed
  Pulse Error
When the value of the threshold is exceeded the designated output will go high allowing for programmable responses via the robot or a connected PLC.
YRC1000 Review
Set threshold and general purpose signal
Threshold
Torque etc.
ON
OFF
General purpose signal
Example: When the actual value is larger than a threshold, automatically turn ON the pre-set general purpose signal

## Slide 11
Inspection Notification Improvements
Displays maintenance critical data with recommended maintenance period
  When to add grease
  When to replace grease
  When to change the wire harness
  When to change the battery
  When to perform an overhaul
Simplify your preventative maintenance planning!
YRC1000 Review
Supply grease
Change grease
Change wire harness
Change battery
Overhaul
Maintenance
Notification R1
Scheduled date
Remaining time
Time in between
Maintenance items
Scheduled maintenance date according to current usage
Supply grease
Change grease
Change wire harness
Change battery
Overhaul
Notification of maintenance before the actual scheduled date
Notification time
Notification number
Maintenance
Notification R1

## Slide 12
Pendant Oscilloscope Improvements
Simultaneous display of:
  Waveform
  Job Content
  Robot Location
Relationship between all easily viewable
  Diagnostic of problem areas
  Optimization
  Performance prediction
YRC1000 Review
3D Robot
Move the cursor left & right
Cursor in the Job is linked and moved up & down