## Slide 2
YRC1000 FSU
Presenter: Greg Smith

## Slide 3: `
FSU Training Overview
  Machine Safety vs. FSU
  Safety Devices
  Enabling FSU/Setup
  Functions
    Axis Range Limiting
    Axis Speed Monitor
    Robot Range Limiting
    Speed Limiting
    Tool Angle Limiting
    Tool Change Monitor
  Files, Signals, & Wiring
    Safety Logic Circuit
    Offline Programming
    Safety Fieldbus Signals
    Stopping Categories
    Hardware
    Loading files onto the controller
    Concurrent Input Output (CIO)
    Expansion Function
  Conflicts & Restrictions
  RIA Requirements
  Troubleshooting
  References
  Hands On Training
Overview

## Slide 4
    What is the Functional Safety Unit (FSU)?
Safety For Humans
  Two parallel Central Processing Units (CPUs) run concurrently on the functional safety board
  Processors function independently to acquire the manipulator encoder feedback in pulse counts
  Based on that position feedback, the functional safety unit can monitor the manipulator and tool’s position, speed, and posture.
  FSU improves the safety of the manipulator’s motion and allows the minimization of nearby overall equipment footprint as well as human accessible areas.

## Slide 5: Machine Safety
Standard and included in all robots
Think protect machines not people
x2 safety rated inputs
x2 programmable outputs
Programmable outputs have Electronic Device Monitoring (EDM) inputs which can enabled/disabled.

## Slide 6: Machine Safety: Safety Logic Circuit
You can use logic on safety inputs and/or a set of signals to trigger an output.
Available inputs: EXESP, FSOUT[n], GSIN[n], GSOUT[n], HOLD, MSOUT[n], #xONEN[n], PBESP, #x PFLIN[n], #x PFLOUT[n], PLAY, PPDSW, PPESP, PROFISAFE, AUXILLIARY RELAY (R[XXX]), REMOTE, S-EXDSW, S-EXESP, S-FST, S-SAFF, #xS-ONEN[n], S-SVON_EN, SAFF, SFBIN[n], SFBOUT[n], #X SFRON[n], SPIN[n], SVON[n], SVONRDY0, TEACH.
Available outputs: #xGSOUT[n] MS-OUT[n], #xPFLIN[x], AUXILLIARY RELAY[XXX], S-EXDSW, S-FST, #x S-ONEN[x], S-SAFF, S-SVON_EN, SFBOUT[x], SVOFF CAT0, SVOFF CAT1
Safety Logic Circuit Page On Pendant

## Slide 7: Machine Safety: With/Without FSU
  Without the FSU you have access to the Safety Logic Circuit, along with the signal allocation and timer delay set.
  The FSU adds:
    Axis Range Limit
    Axis Speed Monitor
    Robot Range Limit
    Speed Limit
    Tool Angle Monitor
    Tool Change Monitor
Without FSU
With FSU

## Slide 8: Safety Devices
Pre FSU
  Zone Rings
  In position switches
  Light Curtains
  Gate Interlocks
  E-Stop
FSU
  Range Limiting
  Axis Limiting
  Light Curtains
  Gate Interlocks
  E-Stop

## Slide 9: Enabling FSU/Setup
Safety Security Level
  FSU is protected from accidental tampering by a requirement to be logged into safety security mode to make changes
  To Change Secuity Mode
    Main Menu > System Info > Security
    With the cursor on Mode, press Select and cursor to Safety mode, then press Select again
    Preset Security Mode passsword
      5555555555555555 (16 fives)
Security Mode Icons

## Slide 10: Enabling FSU/Setup
Functional Safety Board FLASH reset
  Reset required after any changes that update safety function related files or parameters
    Enabling the functional safety unit
    Loading functional safety function-related files/parameters
    Tool calibration or editing of tool load & center of gravity
    Editing home position
  Reset Procedures
    Login to Maintenance mode and Safety Mode level permissions
    From the main menu go to FILE>INITIALIZE
    Select Functional Safety Board FLASH Reset and press enter
    Select YES when the dialog box appears
Note: After completing the above procedures a restart is required to regain full robot operation

## Slide 11: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor
YASKAWA
YASKAWA
YASKAWA

## Slide 12: Axis Range Limit Function
User can set and monitor each axis of the robot and/or auxiliary axes to maintain position within the set limits
32 range files available
  Each file can monitor up to a 6-axis robot and 3-external axes.
Application Uses:
    Alarm=ON  Limit robot range much like hard-stops but infinitely adjustable and can be enabled/disabled via “SIGNAL”
    Alarm=OFF  Monitor external axis or robot position.
      External axis  “At Side A/B” without switches
      Robot  “Robot At Home” without switches (safety-rated cube)
Limitations:
    Axis limits are updated based on projected path and may turn off safety outputs sooner than expected

## Slide 13: FSU Pendant Screens Axis Range Limit
Main Elements
  Function Disable Mode
  32 files available
  File Status
Restricted operations when FUNCTION DISABLE MODE is set to OFF
  Play back operation
  Forward and Backward operations
  Test-run operation
  I/O Jog operation
  Execution of motor gun auto tuning
Security level required to disable
Safety Mode by default
Can be changed in SETUP>OPERATE COND. to any level
Screen shows overall status of all files.
Allows programmer to recover an axis out of range in teach mode

## Slide 14: File Status Guide
Value | Meaning
SETTING | The condition file is still being setup. Monitoring is not performed
CONFIRMING | Confirming the area after the data is set. The status of the monitoring operation depends on the valid condition of the condition file.
VALID (FILE) | File is set and being monitored
INVALID (FILE) | File is set but there is something about the file which makes it invalid
VALID (SIGNAL) | Data setting is completed and monitoring status of the file is in valid status by the establishment of the safety signal condition
INVALID (SIGNAL) | Data setting is completed and monitoring status of the file is in invalid status by the disestablishment of the safety signal condition

## Slide 15: Axis Range Limit Condition File

## Slide 16: How To View Axis Angle Values
Obtain degree measurement for Axis Range Limit Files
    From the main menu select SETUP>FUNCTION ENABLE
    Set ALL AXES ANGLE DISP FUNCTION to VALID
  View current position
    From the main menu select ROBOT>CURRENT POSITION
  Under the top DISPLAY menu, select ABSOLUTE ANGLE

## Slide 17: Example of Axis Range Limit
File 1 – Set as Valid (On), no alarm when tripped, monitoring S1 Axis 1 to stay between -179.5 and -180.5 degrees. When true it will activate FS-OUT01.

## Slide 18: Axis Range Limit Coasting Value
Coasting value is the distance moved after an external axis has been stopped. This value is used to look ahead to ensure the axis stops within the limit.
When using the axis range limit function, or the robot range limit function on an external axis, the coasting value must be set.
Even when stop functions are not used, the coasting value must be set. When the value is not set, The immediate stop must be verified before operating will occur. This will stop remote devices from starting the robot until acknowledged

## Slide 19: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor
YASKAWA
YASKAWA
YASKAWA

## Slide 20: Axis Speed Monitor Function
Set individual axis upper limit speed range for the robot and auxiliary axes and monitors the axes to maintain set limits. Each file can be configured for a single robot, base, or station axis.
One file includes 6-axis robot and 3-auxilliary axes for a single control group. 32 file settings available.
  Application Uses
    Ensuring robot/external axis speed when operator is in a collaborative space.
  Limitations
    This function will not “Command” the robot/external axis to travel at a lower speed. Instead the robot must already be below the set speed. If the axes are moving faster than the setting, an alarm will occur.
  Note: Use the “Speed Limit” function to actively change operating speed.

## Slide 21: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor
YASKAWA
YASKAWA
YASKAWA

## Slide 22: Robot Range Limit Function
Function is used to monitor robot flange center point (FCP) and allow motion inside or outside a user defined shape. If a tool interference is defined, the TCP will be monitored.
32 file settings available for an individual robot or base.
  Application Uses
    Inside or Outside of zone monitoring
  User Defined Shapes
    Planar
    Cuboid
    Prism
  CPU Usage
  Combining safety areas
IMPORTANT!
While the manipulator is in operation, based on motion speed, this function calculates the coasting value, in case of immediate stop by alarm. Then, including the coasting value, the function monitors the safety range.

## Slide 23: Robot Range Limit Tool Interference
Extends monitored are of robot to include tool mounted to T-Flange
Tool file interference changes with programmed tool and selected tool in teach
32 file settings available for an individual robot or base.
  Tool Definition
    Model Tool with 5 “cylinders”
    Tool file interference changes with programmed tool and selected tool in teach.

## Slide 24: Zone Monitoring
  Inside Range Monitoring
    The function is used to monitor the robot and its tool to remain “inside” a user defined shape.
  Outside Range Monitoring
    The function is used to monitor the robot and its tool to remain “outside” a user defined shape.
  Planar Monitoring
    Define a plane in the XY, YZ, or ZX coordinates. The function is used to monitor the robot and its tool to not allow the robot to pierce the user defined plane.
Restricted area
Permitted work area
Restricted area

## Slide 25: Inside Range Monitoring

## Slide 26: Planar Interference Monitoring

## Slide 27: Range Limit Shape Types
Cuboid | Prism
A cuboid is create by defining two points on the XYZ plane to create a cuboid by regarding the connecting line as its diagonal line. | A prism is created by defining the number of points, the coordinates of each point (XY), and setting a Z minimum and maximum for the shape.

## Slide 28: Defining a Range Limit

## Slide 29: Robot Range Limit CPU Usage
  No Free Lunch
    Robot range limit function can, to some extent, freely define the shape as its motion range.
    However, the time period needed for processing the monitoring varies depending on the shape or the method of monitoring
    CPU usage can not exceed 100%
    It is suggested that only one file be active at a time for any one robot. Use FSU inputs to switch files.
  Note that on multiple robot integrations (DRC, TRC) there is only 1 CPU calculation. When exceeding 100%, the following alarms may occur
    Alarm 500 Segment Proc Not Ready
    Alarm 1899 F-Safe Monitor Execute Time over
  Backup file is named RBTRNGLMT.DAT
Chart for general CPU usage estimation

## Slide 30: Combining Two Safety Areas Using “OR” Logic

## Slide 31: Combining Two Safety Areas Using “AND” Logic

## Slide 32: Example Robot Range Limit
AW52C Example
  Allows programmer to recover a robot out of range in teach mode.
    Restricted Functions During Disable:
      Play back operation
      Forward and Backward operations
      Test-run operation
      I/O Jog operation
      Execution of motor gun auto tuning

## Slide 33: Example AW52C – Robot Range Limit
File 1
  File Valid Cond = Signal
  FSBIn1 Play = ON
X+
Y+
Point2
1300,950,1500
Origin
Center S Axis
Point1
-500,-950,-1000

## Slide 34: Example AW52C – Robot Range Limit Cont.
File 2 Play Safe (Both doors Open)
  File Valid Cond = Signal
  FSBIn1 Play = Off
  FSBIn2 Door1Closed = ON
  FSBIN3 Door2Closed = ON
X+
Y+
Point2
500,950,1500
Origin
Center S Axis
Point1
-500,-950,-1000

## Slide 35: Example AW52C – Robot Range Limit Cont.
File 3 Play Work Sta1 (Actually Sta2 ok to work)
  File Valid Cond = Signal
  FSBIn1 Play = Off
  FSBIn2 Door1Closed = ON
  FSBIN3 Door2Closed = Off
X+
Y+
Origin
Center S Axis
Point2
700,950
Point3
700,75
Point4
1300,75
Point5
1300,-950
Point1
-500,950
X+
Point6
-500,-950

## Slide 36: Example AW52C – Robot Range Limit Cont.
File 4 Play Work Sta2 (Actually Sta1 ok to work)
  File Valid Cond = Signal
  FSBIn1 Play = Off
  FSBIn2 Door1Closed = Off
  FSBIN3 Door2Closed = On
X+
Y+
Origin
Center S Axis
Point4
1300,-75
Point3
1300,950
Point4
700,-75
Point6
700,-950
Point1
-500,-950
Point2
-500,950

## Slide 37: Programming Robots Near FSU Barrier
High Speeds in Play Mode
  When running the Manipulator at full speed near the limit of a virtual zone it will calculate the look ahead distance.
  Even though the end point is inside of the cube, it will often generate this alarm.
    “F-SAFE ROBOT RANGE LIMIT INTFERENCE”
  Work Around
    Slow the robot way down before making its next turn.
    Exact settings should be customized in an application specific manner.

## Slide 38: Programming Robots Near Robot Range Limit Demo

## Slide 39: Programming Robot Range Limit Cont.
  Main Zone
    Create a robot range file for the zone you want the robot to stay within.
  Slow Down Plane
    Create a second file using a plane coordinate.
    You will want this wall to be close to the current wall you are approaching. Designate which output signal you want to use. Here we are using
    FS-OUT1.
  Under Speed Limit
    Create a file under Speed Limit. Enter the desired speed and Detection Delay time.
    Create your safety logic file using the logic tied to your robot range and speed limit file.
    Adjust the X-Y plane as needed. This will allow you to run at full speed until it crosses the plane, then it will slow down to the speed you allocated in your Speed Limit File without an alarm.

## Slide 40: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor
YASKAWA
YASKAWA
YASKAWA

## Slide 41: Speed Limit Function
  Controls TCP/FCP Speed
    Limits robot’s tool center point (TCP) speed or flange center point (FCP) to maintain set limits.
    When “zero” is set as the speed limit for the robot or auxiliary axes. This is referred to as stop state monitoring.
  Application Uses
    Provide a safe stop state for operators to interface with the equipment for purposes of loading/ unloading part fixtures or tip-change/dress for arc/spot welding applications.
    Stop-state monitor “Operator side” of positioner while part processing takes place on robot side of positioner (similar to servo disconnect but power still remains on operator side ).
Flange Center
Point (FCP)
Tool Center Point (TCP)

## Slide 42: Speed Limit Function Cont.
  Limitations
    Depending on implementation, once the triggering signal is cleared (For example a light curtain) full-speed operation may resume.
  Stopping Times
    When limiting speed stopping times must be measured for safety distance calculations.
SPDLMT.DAT Backup file for Speed Limit Function Data

## Slide 43: Example of Speed Limit Function

## Slide 44: Speed Limit Function Standard Product Example
  AW6X00 Standard Product
    Standstill Trunion (S1) axis if positioner is at side A or B and light curtain is invaded
    Standstill Side A (S2) tooling Axis if light curtain is invaded and SideB is at robot
    Standstill Side B (S3) tooling Axis if light curtain is invaded and SideA is at robot
    E-Stop still stops positioner while rotating.
Light Curtain
Light Curtain
Speed is limited when input turns off (Set = on), and file becomes valid

## Slide 45: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor

## Slide 46: Tool Angle Monitor Function
  Restrict Undesirable Angles
    Provides the ability to set tool angle limits and monitors the tool to maintain position within the set limits.
    Function can maintain multiple tools of different shapes and sizes when using the robot range limit function.
  Application Uses
    Tools with dangerous end effectors (lasers, nail guns, etc.)
    Tools which must maintain a specific angle (paint, glue application, etc.)
  Backup file
    TLANGMON.DAT

## Slide 47: Tool Angle Limit Function

## Slide 48: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor
YASKAWA
YASKAWA
YASKAWA

## Slide 49: Tool Change Monitor Function
  Monitors the tool file used in the functional safety function to be consistent with the user specified tool file.
  Prevent Undesirable Tool Use
    Ability to switch between multiple tools of different shapes and sizes when using the robot range limit function.
    16 individual rule “file” settings available.
  Steps to use function
    Set the tool file
    Set the tool interference file
    Set the tool change monitor function
    Confirm the tool change
    Start the tool change monitor function
NOTE: Must enable Tool Change Monitor function in Maintenance Mode to use

## Slide 50: Functional Safety Unit Features
YASKAWA
Axis Range Limiting
Axis Speed Monitor
Robot Range Limiting
Speed Limiting
Tool Angle Limiting
Tool Change Monitor

## Slide 51: Signals & Wiring – Safety Logic Circuit
  The safety logic circuit is an intuitive to create on the programming pendant.
  It enables to set up the logical operations, such as stopping the manipulator or outputting a signal if the servos are on.
  Function I/O Logic
    Files can be set to become valid based on FSU signals.
    Up to 5 input signals can be used in series (AND)
    To implement “OR” conditions use multiple files

## Slide 52: Functional Safety Board (FSB) Inputs
Standard with every YRC1000 controller is the Safety Board which provides 2 safety inputs and outputs (GSIN1-2 and GSOUT1-2).
An optional safety I/O expansion board (ASF02) can be purchased. This gives access to FSBIN1-8 and FSBOUT1-8.

## Slide 53: Signals & Wiring – Safety Logic Circuit
  Available Inputs
    PLAY, TEACH, PPESP, PPDSW, PBESP, EXESP, EXDSW, SAFF, GSIN1, GSIN2, SVON, & AUX RELAY (R[xxx])
  Available Outputs
    GSOUT1, GSOUT2, SVOFF CAT0,
    SVOFF CAT1, AUXILIARY RELAY(R[xxx])
  Features
    128 Lines of Logic
    2 ms scan time
    2 input signals 1 output signal per line.
    Backup File YSFLOGIC.DAT
You can use logic on safety inputs and/or a set of signals to either trigger an output, or an emergency stop.

## Slide 54: Signals & Wiring – Safety Logic Circuit
Input Signals
Logic Signals
Logic Operators

## Slide 55: Offline Logic Programming
Offline programming available in MotoSim
Supports inform software version 1.8+
Software key required to run MotoSim
Create YSFLogic.dat file to load into controllers
Decrease startup time

## Slide 56: Safety Fieldbus Signals: SFBIN/SFBOUT
Optional function
64 signals (1-64)
Signals can be used by Machine Safety Board or Functional Safety Board
Setting | Meaning
NOT USE | Neither
M-SAFE (YRC1000) | Machine Safety Board (can be used in Safety Logic Circuit)
F-SAFE #1 (YRC1000) | Lone Functional Safety Board

## Slide 57: Stopping Categories
  Stop Category 0
    The immediate insulation of the motor power source to servo motor causes the stop.
    After the motor power is insulated, the manipulator and the external axis decelerate by the brake and stop
    The manipulator and the external axis may run off the operating path.
  Stop Category 1
    The manipulator and the external axis are controlled on the operation path, decelerate and then stop.
    After the stop, the manipulator and the external axis are locked by the brake and the motor power is insulated.
  Stop Category 2
    The manipulator and the external axis are controlled on the operation path, decelerate and then stop.
    After the stop, the position is retained in a state that the motor power is being supplied.
Stopping Manipulator Operation
The following three categories are manipulator stop functions.
YRC1000 Stop Categories

## Slide 58: Hardware Requirements
  Safety rating Cat 3, PL d
    Mean Time To Failure for each channel 36 years
    5.16x10-7 probability of failure per hour
  Stopping Category
    FSU Functions trigger a category 0 stop
  Caution
    Verify installed device safety rating before use
  Multiple robot configurations available
Source: ab.com

## Slide 59: Hardware Components
  Safety Board JANCD-ASF01-E
    Safety board standard on all YRC1000 controllers.
  Machine Safety I/O Interface Board
    Mounts and plugs into the safety I/O board.

## Slide 60: Hardware Components
  JANCD-ASF02-E
    Expansion safety I/O
    8 safety inputs/outputs (FSBIN1-8 and FSBOUT1-8)
  Machine Safety I/O Interface Board
    Mounts to YRC1000 door and connects to ASF02 board.

## Slide 61: FSU - Hardware - I/O interface board
  Inputs
    8 Dual Channel
    2 Channel sourcing (24 VDC)
    Discrepancy timing
    Multiple FSU functions can run from 1 dual channel input.
      For example: door closed input 1 can activate range limiting and speed limiting
    Must add relays to transistor output safety devices.
  Outputs
    8 Dual Channel
    2 Channel sourcing (24 VDC)
    EDM can be configured to verify N/C monitor contact.

## Slide 62: File Loading/Saving
  FSU files can be loaded into the controller
    In order to upload MotoSim files to the controller, you must first disable CRC check.
    Saving files can be done in any mode but loading must be conducted in Safety Mode.
  Load/Save Procedure
    EX MEMORY>LOAD or SAVE > FILE/GENERAL DATA> Select File > Press Enter > Press Yes
Note: After loading FSU related files, the “Functional Safety Board FLASH Reset” message appears in maintenance mode until the FSB Flash is reset.
File Data Type | File Name
Axis Range Limit | AXRNGLMT.DAT
Axis Speed Monitor | AXSPDMON.DAT
Robot Range Limit | RBTRNGLMT.DAT
Robot Speed Limit | SPDLMT.DAT
Tool Angle Monitor | TLANGMON.DAT
Tool Change Monitor | TLCHGMON.DAT
APPR Warning Buzzer Data | APPRBUZR.DAT

## Slide 63: File Loading/Saving Errors
  Alarm 0300 Verify Error (System Config-Data) [10] Causes
    Data related to this function was loaded from an external storage.
    The home position calibration or the home position change operation was performed.
    The tool calibration operation was performed.
    The data saving has not been performed correctly.
    The zeroing function was performed.
  Solution
    Functional Safety Board FLASH RESET
    Slide 10 for procedure

## Slide 64: CIO
  Signals
    Function signals are available in CIO for all 32 files (only 2 shown here).
    File valid, monitoring results valid, disable
Speed Limit
Robot Range Limit
Axis Range Limit
Axis Speed Monitor
Function Disable Modes

## Slide 65: CIO Cont.
  Safety Fieldbus
    Inputs 1-64
    Outputs 1-64
  FSB
    Boards 1- 8
    Inputs 1-8
    Output 1-8
  Safety Logic Circuit
    MS Out 1-64
  Functional Safety logic circuit
    FS Out 1-64

## Slide 66: Conflicts and Restrictions
  Functions which modify parameters or files during Playback Operation cannot be Used Concurrently with Functional Safety Unit
  Data of parameters or files are saved in a duplicated manner and are checked for safety.
    When modifying this data, special procedures such as read back operations or re-setting of the FLASH data are required.
    For this reason, functions that modify parameters or files when executing during play back operation cannot be used concurrently with the functional safety unit.
  Examples
    T-axis speed control function
    PMT function (SETTOOL instruction)
    ToolSight (Ok if only used to check TCP and not adjust robot jobs

## Slide 67: Conflicts and Restrictions Cont.
  MotoCal
    If required, perform Motocal on a robot prior to turning on FSU
    ABSO data has CRC data check when FSU is turned on
    For this reason, functions that modify parameters or files when executing during play back operation cannot be used concurrently with the functional safety unit.
  FSU Master / Slave Configuration
    When using FSU in a multiple robot control configuration, the master controller must have FSU installed
    Slave controller is optional
  Conveyor Tracking and COMARC software options
    In these options the speeds are added along with the normal operation speed.
    TCP or flange speed may not be able to be controlled as specified.
      Alarm 4785: F-SAFE SPEED MONITOR ERROR
      Countermeasure: Se the limit on the condition file with the calculated value on the basis of the speed added by the function.
  Motor Gun Function
    Only the axis range limit function and axis speed monitor function are available to the motor gun.

## Slide 68: Conflicts and Restrictions Cont.
  Servo Float Function
    Manipulator and feedback position/speed may differ greatly when enabled.
    If FLOATON is active the results of instruction/feedback monitoring may vary.
  MotoPlus
    When using the path correction function or the increment level movement function in MotoPlus, the speed limit function is not available.
  MotoFit
    When using the path correction function or the increment level movement function in MotoFit, the speed limit function is not available.
Data | Operation | FSU Avail | No FSU
Tool File | Editing on the tool file screen | SAFTEY SECURITY MODE | EDITING SECURITY MODE
 | Tool calibration |  | 
 | Auto measuring of tool load/cent. gravity |  | 
 | Loading from external memory |  | 
 | File initialization in maint. mode |  | 
Tool Interference File | Editing on the tool interference screen |  | 
 | Loading from external memory |  | 
 | File initialization in maint. mode |  | 
Home Position | Edit in the ABSO data screen |  | MANAGEMENT SECURITY MODE
 | Loading from external memory |  | 
 | File initialization in maint. mode |  | 
 | Zeroing software option |  | 
Individual Parameters | Loading from external memory |  | 
 | File initialization in maint. mode |  | 

## Slide 69: RIA Requirements
  Major Changes to ANSI/RIA 15.06 Safety Standards
    Risk Assessments now required for all robot cells
    Assessment should determine safety requirements for cell
    Must be completed by certified safety inspector
  Change in the control of robot motion to include safety-rated soft axis and space limiting features
    Section 5.12 Axis Limiting
      Yaskawa Functional Safety Unit (FSU) category

## Slide 70: Demo Lab Exercise
1. Create a Robot Range Limit keeping robot INSIDE specified volume. Alarm = ON.
2. Create a new Robot Range Limit (OUTSIDE), that triggers a Speed Limit when robot enters the volume.
3. Wire dual channel safety switch to GSIN#1(YRC1000) to conditionalize whether the Speed Limit is valid or not from (2).
4. Use ‘3D Graphics Display’ to monitor robot and Robot Range Limit position.

## Slide 71: Demo Lab Exercise Continued
5. Configure EDM to a safety output
  Configure GSOUT2 feedback to ‘USED’ in Maintenance Mode.
  Wire force guided relay
    GSOUT2_1+/GSOUT2_1- should power relay
    GSIN1 should be wired to NC relay contacts.
  Define GSIN1 as EDM feedback for GSOUT2 in Safety Logic Circuit.

## Slide 72: Demo Lab Exercise Continued
6. Define FSU settings in MotoSim, load into real controller.
  Disable CRC check
  Monitor M-registers for CRC value. Convert M-Registers to match CRC value.
    Hint: CRC Value = MReg1 + (MReg2*65536)
Example:
49038 + (22851*65536) = 1497612174