## Slide 2
External Axis Installation and Set-up
Presenter: Rick Vaught

## Slide 3
ESD Protection
Use a static strap to protect boards from damage by ESD (Electrostatic discharge)
Put wristband on.
Connect alligator clip to a ground lug in the controller.
Step 1

## Slide 4
The 164290-1 servo control board for Axis 7,8 and 9 is a daughter board that mounts to the right side of the robots servo control board.
This board comes with standoffs that screw into the EAXA21A (robot servo control board) inside the DX200 controller
Step 2 – Installation of the Servo control board

## Slide 5
Remove mounting screws from the side of the EAXA21A board where the external axis servo control board will be mounted.
Note – if you are unsure as to which screws to remove, hold the external axis servo control board up to the robot control board for comparison
Mounting the servo control board
Removed screws.
Keep the screws that have been removed

## Slide 6
Mounting the servo control board
Replace the removed screws with the standoffs that are provided.
Snug the standoffs but do not overtighten

## Slide 7
Mounting the servo control board
There is a “male” connector on the back of the external axis servo control board.
Line the board up with the female connector on the DX200 EAXA21A board and plug in.
The mated connectors should support the board (temporarily) and observe that the through holes of the board line up with all of the standoffs that were installed.

## Slide 8
Mounting the servo control board
Using the screws that were removed from the DX200 EAXA21A board, screw down the servo control daughter board for the external axis
Note : replace all removed screws. Only 3 are shown in picture as example
Replaced screws

## Slide 9
Mounted servo control board

## Slide 10
Step 3 – Preparing the Amplifier for Installation
The amplifier comes with a thermal sheet (ref. notes section of prints).
Remove the protective film from each side of the thermal sheet.
Place the thermal sheet on the metal on the back of the amplifier.
Remove film on thermal sheet
Thermal sheet placed on amplifier

## Slide 11
Step 4 – Installing the amplifier
Find the release pins on the amplifier module located at the right of the module on the top and bottom and gently pull out until you feel a click.

## Slide 12
Step 4 – Installing the amplifier
After the pins on the amplifier module have been released, the front panel opens and swings on hinges to reveal the robot amplifiers and the 3 spots for additional external axis amplifiers.
Space for additional amplifiers
Door closed
Door open

## Slide 13
Step 4 – Installing the amplifier
Per print, install the correct amplifier using the correct hardware as designated by the bill of material (BOM).

## Slide 14
Step 5 – amplifier connections
Back of DX200 controller
Remove lower right back panel
Prepare the controller for the installation of the encoder and power pigtails.
Remove the M4 screws and remove the cover plate.
Save the screws to remount the cable entry panel.

## Slide 15
Preparing the cable entry panel
*note * The parts that are shown here are for this particular external axis kit, other kit parts will not be exact part numbers but resemble the example
Feed the cables through the appropriate openings of the panel. Using 8, M4x12 PPH screws (137146-4), attach the bulkheads of the cable assy to the cable entry panel. Make sure the orientation of the bulkheads matches the print.

## Slide 16
Installing the cable panel
Feed the cable ends through the opening in the DX200 controller

## Slide 17
Ground wire attachment
Before securing the cable entry panel, connect the ground wires from the encoder cable assembly and the power cable assembly to the ground plate located in the back of the controller
Also, connect 168718-1, 14 awg ground jumper from the ground post on the cable entry plate to the ground plate of the controller.

## Slide 18
Amplifier connections

## Slide 19
Connection of Amplifier interface cable, 168398-()
Connect amplifier interface cable to the CN581 of the amplifier.

## Slide 20
Connection of Amplifier interface cable, 168398-()
After connecting the cables to the amplifier, route the cables through the right side of the chassis of the amplifier module. And let hang free at this point.

## Slide 21
Connection of 168365, DC control power to Converter
Remove dummy plug CN552B from the converter module in the DX200 and plug in the 6 pin connector, marked CV1-CN552B of the 165365-2 cable.

## Slide 22
DC control power cable connection to amplifiers
Plug in connector “amp 7 CN582” to the CN582 connector on amp 7

## Slide 23
Installation of Converter power cable
Remove the dummy plug from the CN558 slot on the converter unit in the DX200.

## Slide 24
Installation of Converter power cable
Plug the connector marked with the label “CN558” into the converter, port CN558.

## Slide 25
Installation of Converter power cable
Neatly route the cable to the amplifiers and connect the connector labeled “Amp 7 CN583” to amp 7

## Slide 26
Installation and connections of power and encoder pigtail from cable entry plate
Power connection : Pull the cables from the pigtail, through the opening in the DX200 controller to the front of the controller.

## Slide 27
Installation and connections of power and encoder pigtail from cable entry plate
Neatly route the power cables through the Panduit channel and up to the amplifiers. Wire tie cables with the existing bundle of robot amplifier power cables.
Wire ties
Power cables
panduit
Brake wires

## Slide 28
Installation and connections of power and encoder pigtail from cable entry plate
Make motor connections at amplifier.

## Slide 29
Brake line connections
The brake wires for the motors are twisted pair, blue and blue/white wires. Separate the brake wires from the motor power cables and route to the YBK01, brake board.
Brake wires

## Slide 30
Brake Board location in DX200
The YBK brake board is located on the back side of the EAXA21A, servo control board rack. To reveal this board, pull the two release pins on the rack and open the door.
Open door
Brake board
Release pins for servo control unit. 2 locations top and bottom.

## Slide 31
Brake wire hook up.
Locate the CN400 connector on the YBK brake board and unplug by squeezing the release tabs on the top and bottom of the connector and pull.
CN400

## Slide 32
Brake wire hook up.
When the twisted pair brake wires have been neatly routed to the brake board, insert the socketed wires into the connector.
The wires are labeled BRK7+, BRK7-
BRK7+ will go into CN400-B4
BRK7- will go into CN400-A4

## Slide 33
Encoder connections
From the encoder limit switch cable, attach the designated grey encoder connection to the external axis servo control board.

## Slide 34
Servo Enable Connector
The final step of the physical set up is the installation of the servo enable connectors.
Plug the connectors in as shown.

## Slide 35
Now that all of the modules, boards and cables have been installed and connected, the external axis needs to be set up in the DX200 controller.
Hold the “Main Menu” button down on the teach pendant while powering on the controller.
Continue holding the “Main Menu” button down until you hear a beep.
When the controller boots up, you will be in maintenance mode. This is where the set up of the external axis is performed.
External axis set up in the DX200

## Slide 36
External axis set up in the DX200
After entering “Maintenance Mode”, you will need to enter the “management” level of security.
Select management mode from the drop down menu and enter sixteen “9’s”

## Slide 37
External axis set up in the DX200
After entering “management mode”, select SYSTEM > SETUP from the menu

## Slide 38
External axis set up in the DX200
The next screen you will see is the SETUP screen.
Cursor down to CONTROL GROUP and select.

## Slide 39
External axis set up in the DX200
The next screen you will see is the CONTROL GROUP screen. From this screen you will select the ROBOT and EXTERNAL AXIS.
Cursor down to the line you want to add the robot and external axis and select on DETAIL.
Once you select on the R1 and S1, as this example will be, a screen with the full machine list will be displayed.

## Slide 40
External axis set up in the DX200
From the MACHINE LIST screen, select the correct machine.
The machines listed describe the type of external axis.
For example, a single rotation head stock would be a TURN-1.

## Slide 41
External axis set up in the DX200

## Slide 42
External axis set up in the DX200
After the machine has been selected the following machine set up screens will follow. This information can be found on the machines specification sheet or designated by your engineering group.

## Slide 43
External axis set up in the DX200

## Slide 44
External axis set up in the DX200

## Slide 45
External axis set up in the DX200

## Slide 46
External axis set up in the DX200

## Slide 47
External axis set up in the DX200

## Slide 49: Fonts and Primary Colors to use throughout PPT
Body copy
Subheads within body copy
Headers on content slides
These are the secondary colors to use throughout the PPT to add color
preferred
add’l if needed
RGB 0-0-0
RGB 237-195 -27
RGB 243-112-33
RGB 132-177-33
RGB 194-216-54
RGB 0-133-63
RGB 29-190-235
RGB 165-51-126
RGB 56-54-135
RGB 0-86-185
RGB 100-101-102
FONT: Arial Bold and Arial Regular