## Slide 1
MotoSight 3D BinPick Product Overview
Yaskawa Sales Update
Pub Talk Series
Tony Kitazawa
Canon U.S.A.
Keith Vozel
Yaskawa Motoman

## Slide 2
The Pub is Open

## Slide 3: MotoSight 3D BinPick Topics
What is MotoSight 3D BinPick
Key Product Features
Technology
Product Advantages
System Architecture
Software Options
Camera Models

## Slide 4: What is MotoSight 3D BinPick
A solution designed for recognizing and picking randomly stacked parts from a bin.
Delivered in partnership with Canon U.S.A, Inc.
  A leading provider of business-to-business and industrial digital imaging technology
Notes: The MotoSight 3D BinPick solutions leverages leading edge 3D imaging and recognition technology through a business partnership with Canon U.S.A. This allows Yaskawa to offer a solution that is specifically designed to recognize and pick randomly stacked parts from a bin. As technology changes and Canon makes improvements, we can easily incorporate those changes into our solution.

## Slide 5: MotoSight 3D BinPick Features
1. High speed recognition
Fast 1.8 sec recognition time (RV300/500). Even faster with option software.
2. Dynamic picking strategies / Collision check
Multiple pick points can be taught. Both of P3 (Approach position) and P4 (Grasp position) can be provided with consideration of collision avoidance against adjacent parts and a bin.
3. Easy setup
Very simple set up. No programming required to register a new work piece - just load a CAD file and take pictures.

## Slide 6: MotoSight 3D BinPick Features
4. High Precision / Repeatability
Precision CAD fitting. High repeatability of 0.1mm (RV300)
5. One time measurement gives 3D position and orientation: 6 DOF
Additional 2D scan is not required – shorter cycle time.

## Slide 7: MotoSight 3D BinPick vs Traditional Methods
One device per one part
Huge - takes space
Noisy
Expensive to modify
Not reliable
Bowl Feeder
Human Operators
Expensive
High turnover
Hard to fill the position
MotoSight 3D BinPick
Flexible – up to 200 parts
24/7 operation
Easy to change parts

## Slide 8: MotoSight 3D BinPick Technology
1. Image capture
2. Quick discovery
4. Feasibility
3. Precise CAD fitting
3D
2D
Space coding by structured light for a fast scan + quality camera generates high quality point cloud and images.
Referring to the pre-learned “Dictionary” made by 3D CG technique enables super fast initial parts discovery.
Collision check, approaching angle limitation, occlusion ratio are determined in order to choose the “Finalist”.

## Slide 9: Advantage- Flexible Part Recognition
Automotive
Metals
Plastics
Electronics

## Slide 10: Advantage- Proven Solution
Printer manufacturer
Toner cartridge parts 100mm×300mm×50mm, Plastic
Home electronics manufacture
Microwave oven parts 100mm×200mm×10mm, Metal
Motor cover 30mm×50mm×10mm, Plastic
Gear parts 50mm×50mm×10mm, Plastic
Electronics parts 170mm×10mm×10mm, Plastic
Automotive - random bin picking
Connecting Rod 100mm×200mm×15mm, Metal
Crankshaft 200mm×500mm×100mm, Metal
Side Member 100mm×1000mm×30mm, Metal
Intermediate shaft 50mm×300mm×50mm, Metal
Automotive - location measurement
Door panel 1000mm×1000mm×20mm, Metal

## Slide 11: Advantage- Quick Installation and Simple Registration
Other 3D
64hrs total
15hrs total
Programming：47.5hrs
3D CAD data upload and shoot picture：6.5 hrs
Canon
Total Operator Hour：64 hrs
Operator working hour：13.5 hrs

## Slide 12: Advantage- Precise Recognition & Solid Picking Strategy
3D recognition
Feed
Directly to the destination
MotoSight 3D
Precise recognition
No additional scan
Shorter cycle time
Up to 200 parts
Precise recognition - No additional scan needed

## Slide 13: Advantage- Precision Recognition and Solid Picking Strategy
Collision check against bin and parts
Takes your EOAT (hand) CAD file
Dynamic grasping strategy creation
Grasp #2
Grasp #1
P3 (X,Y,Z)
P4 (X,Y,Z)
P3 (X,Y,Z)
P4 (X,Y,Z)
multiple grasping can be taught

## Slide 14: System Architecture
DX200 or YRC1000
Robot
PC, Interface Software, Recognition Software
Power Supply
Ethernet Cables
DC cable
Vision Head

## Slide 15: Optional Software
Consecutive
Recognition
option
Multi-Bin
Recognition
option
Partial CAD
Recognition option
Slider
Option
Need for
higher speed
or
solution for
kitting
Need to handle
huge and
flexible parts
Need to cover
wider or deeper
area

## Slide 16: Option- Multiple Bin Recognition
Multiple bins can be recognized by one scan - shrink the cycle time
Standard
Recognizes 1 area only
Area 4
Area 1
Area 2
Area 3
or
Area 1
Area 2
Area 3
Area 4
Multiple bin recognition per 1 shoot (requires option SW)

## Slide 17: Option- Multiple Bin Recognition
Shoot
Robot pick up #1
Rec
Robot pick up #2
Robot pick up #2
MV
Robot
1.8[sec]
1.8[sec]
2.4[sec]
MV
Robot
Standard RV500
Measurement time per 1 work piece
1.8 sec
w/ Option SW
Measurement time per 1 work piece
1.2 sec
Robot pick up #1
1 shoot recognizes 1 area
1 shoot recognizes 2 areas
Shoot
Rec
Shoot
Rec
Rec

## Slide 18: Option- Consecutive Recognition
After pick #1, reuse the existing full scan image if possible
Perform a full scan and provide a pick #1 candidate
After the pick, take a quick picture and check if new scan is needed
If other than #1 is NOT changed, skip a full scan and provide pick #2 candidate using an existing picture.

## Slide 19: Option- Consecutive Recognition
Robot pick #1
Robot pick #2
Robot pick #2
MV
Robot
1.8[sec]
1.8[sec]
1.8[sec]
MV
Robot
Robot pick #1
Rec
1.0[sec]
Shoot
Rec
Shoot
Rec
Shoot
Rec
Detect
Change
Standard RV500
Measurement time per 1 work piece
1.8 sec
w/ Option SW
Measurement time per 1 work piece
1.4 sec
After the first pick, take a short picture and check if additional full scan is needed. If not, reuse existing picture and gives #2 pick candidate

## Slide 20: Option- Partial CAD Recognition
Recognize large parts or the parts with some flexible portions, using partial CAD
Example of large parts exceed the measurement area
Partial CAD

## Slide 21: Option- Partial CAD Recognition
Another usage – let MotoSight 3D recognize the solid portion only (ignore flexible cable portion that cannot be CAD fit)

## Slide 22: Option- Slide Mount
Attach the camera to a slider and measure from multiple positions
Ideal for :
handling multiple bins
measuring a greater area
High volume production where frequent bin exchange is needed

## Slide 23: Option- Slide Mount
When right bin becomes empty, moves to left automatically.
Application example:
Another usage – by mounting on a vertical slider, deeper area can be covered.

## Slide 24: Camera Models
Based upon part size and bin size
 | RV300 | RV500 | RV1100
Measurement Range H x W x D (bin size) | 340 x 340 x 100 | 540 x 540 x 200 | 1160 x 1160 x 600
Minimum Part Size | 10mm x 10mm | 20mm x 20mm | 45mm x 45mm
Recognition Time | 1.8 sec. | 1.8 sec. | 2.5 sec.
Working Distance | 500mm | 800mm | 1750mm
Camera Cycle Time | 3 sec. | 3 sec. | 5 sec.

## Slide 25: Coming Attractions
What else is needed to help you sell Yaskawa Vision Solutions?
  Email suggestions to keith.vozel@motoman.com
        takitazawa@cusa.canon.com
Have any questions?
  Email questions to keith.vozel@motoman.com
        takitazawa@cusa.canon.com
  Questions and answers will be distributed to all attendees

## Slide 26
The Pub is CLOSED